The Multical 403 is a heat, cooling and heat/cooling energy meter for the household and small industrial facilities sector. Measuring range from 6 l/h to 30,0 m3/h (Dn15... Dn300).

Standard set: calculator with D-type battery, integrated flow part with signal cable 1.5 m, temperature sensor pair Pt500 with cable length 3m, sensor shells 65 mm. Adateative directing 4...64 sec. (fixing parameters for calculation depending on changes in system parameters).

Freely programmable for forward or backs pipeline (by default in forward mode) before counting the first litre.

Special kit options
Variants of temperature sensors:
Pt500 2-strand with cable length 1.5 m or 3.0 m.

Feeding:
D-type battery
230 VAC
24 VAC

Data communication capabilities:
Data (RS232) + 2 pulse inputs;
Data (RS232) + 2 pulse outputs;
M-Bus;
Wireless M-Bus;
Analog outputs 2x4... 20 mA;
ModBus RTU (RS-485)
u.c. See section "Meter equipment"