Multical 803 is a heat, cooling, heat/cooling and glycol energy meter for the industrial object sector. Measuring range from 6 l/h to 2000,0 m3/h (Dn15... Dn300).

Standard set: calculator with power supply 1 x 230 VAC or 24 VAC/VDC module, flow part Ultraflow X4 with signal cable 2.5 m, temperature sensor pair Pt500 with cable length 3m, sensor shells 65 mm. Fast integration mode 2 sec. (fixing parameters for calculation).

Freely programmable for forward or backs pipeline (by default in forward mode) before counting the first litre.

Special kit options
Signal cable strap calculator and flow part:
2,5 m
5 m
10 m
10...30 m
30...100 m.

Variants of temperature sensors:
Pt500 2-strand (for shells)		Pt500 4-strand (submersible)		Pt500 or Pt100 4-strand (for shells)
Shell length options	Cable length options	Sensor depth capabilities	Kabeļu garumu iespējas	Sensor depth options	Shell length options	Cable length options
65 mm	1,5 m	90 mm	> 100 m	105 mm	85 mm	> 100 m
90 mm	3,0 m	140 mm		140 mm	120 mm
140 mm	5,0 m	180 mm		230 mm	210 mm
	10,0 m

Feeding:
230 VAC
24 VAC/VDC

Data communication capabilities:
Data (RS232) + 2 pulse inputs;
Data (RS232) + 2 pulse outputs;
M-Bus;
Wireless M-Bus;
Analog outputs 2x4... 20 mA;
LON;
ModBus RTU (RS-485);
ModBus/KMP TCP/IP;
u.c. See section "Meter equipment"